MULTITOUCH FOR PUREDATA

Enabling pseudo-multi-touch mode
with pd-native guis, inside any patch.
Demo here : https://vimeo.com/292789121
## Setup
- OS : linux
- Hardware : pc with multitouch screen.
- Puredata >= 0.49
- Externals : iemguts lib, hcs/screensize (optional)
- A patched version of hidio external, that reads screentouch events.
## How it works
The multitouch events from touchscreen device are captured with hidio external. Then, they are converted into serialized mouse events (i.e. for each touch event, one message mouse immediately followed by a message mouseup with an offset corresponding to the finger movement). Those messages are sent to the active patch window.
## Configuration
- Required configuration : linux pc with multitouch screen.
- Multitouch gestures (scrolling, zooming, pinch, etc...) shoud be desactivated on the O.S.. Only monotouch events have to be forwarded as mouse events by the O.S..
- Puredata 0.49
- hcs/screensize external (optional)
- iemguts lib externals
- and a special version of hidio (included). see here https://github.com/jyg/PdMultitouch/blob/master/hidio/Readme.md
## Installation
1. check you have installed iemguts externals library.
2. put the hidio.pd_linux file (from hidio folder) into your externals folder. Check if it works by opening hidio-help.pd. (If not, you may have to recompile it. In a terminal inside hidio folder, type ./configure then make).
3. Open the patch multitouch.enable-help.pd.
4. follow the 3-stages configuration in the multitouch.settings.pd window.
That's all...

https://forums.opensuse.org/showthread.php/506695-Multitouch-on-ELAN-touchscreen

https://www.kernel.org/doc/Documentation/input/multi-touch-protocol.txt